## Slide 1: DT Overview 2016 by Robin T. Miller Robin.Miller@wdc.com A Simple Tool With Unique Features! 
21 December 2016

## Slide 2: Preface
Why are we here today? Well, it’s not for:
  why is #21 Robin’s favorite number?
    no, it’s not because of Las Vegas, NV! 
    it’s Roberto Clemente, Pittsburgh Pirates
  who wrote “The Five Fundamentals of Golf”?
    that’s Ben Hogan by the way!
We’re here to talk about this tool named DT!

## Slide 3: Wide Audience
Folks Who Write Automation for DT
  options, test cases, workloads, etc
Folks Who Use Automation with DT
  what is DT doing, how to debug issues?
Folks Who Are Curious What DT is About
  what can DT do, and why should I use it?
Focused Presentations Are Available
Whatever Your Interest, Hopefully This Presentation will Whet Your Appetite! 

## Slide 4: Agenda
Short History
Key Features
Tools, Tools, Tools
DT Use Cases
Feature Overviews
Documentation
Where is DT Located?
Other Useful Links
Q&A

## Slide 5: Short History
Originally Developed for Testing Tapes
  this is where the write/read pass originated
  unit test tool to replace Unix dd/cmp tools!
  dt options share those of the Unix dd utility
Disks and File System Extensions Added
I/O Monitoring to Detect Slow or Hung I/O
I/O History Added to Help with Corruptions
Corruption Analysis (for IOT pattern)
Block tags for Higher Data Validation
Open Source, uses BSD license
Been Pet Project for nearly 30 Years Now! 

## Slide 6: Key DT Features
Script / Startup Files
Interactive Mode
Multi-Threading
Multiple Log Files
Dynamic Job Control
Multiple Device Support
Extended Error Reporting
Corruption Analysis
I/O Monitoring
Retry Errors
SCSI Options
Block Tags
I/O Percentages
Workload Definitions
Predefined Workloads
Trigger Types

## Slide 7: Tools, Tools, Tools…
Today, there is no perfect I/O Tool! 
Why choose DT? (a couple reasons)
  flexibility (roll-your-own tests/output)
  data pattern control / data validation
  triage options, supported, and maintained!
What about fio or iozone or netmist?
  main focus is performance (latency, etc)
  data validation is limited (or missing)

## Slide 8: Choosing The Appropriate I/O Tool
#1 What Are Your Specific Test Goals?
What’s Most Important?
  Data Validation (should be important, IMO)
  Data Duplication (compression / dedup)
  Cloning, Mirroring, or Snapshots (verify data)
  Maximum Throughput / Performance Stats
  File System Operations (File Locking, etc)
  Scale Out to many Disks and/or Volumes
  Troubleshooting Features
  Timing I/O (for System Level Agreement)
Note: DT developed for Device Qualification

## Slide 9: Why Choose This DT I/O Tool?
Easy To Use… well, Robin thinks so! 
File System and Direct Disk Support
I/O Monitoring for SLA Requirements
Debug and Troubleshooting Features
  key to help triage and root cause issues!
Multi-threaded with multiple log files
Extensive Documentation & User Community
Maintained and Supported, Why Important?
SCSI Information, I/O and error reporting
Evolving based on Product/User Requirements

## Slide 10: DT Use Cases
Data Generation and Verification
File System Buffer Cache control
Dynamic Throttling of I/O’s (IOPS)
File/LUN Copy/Verify or LUN Clone/Verify
Large Terabyte LUNs and Volumes
Sparse File Testing (holes in files)
Supports any Disk Sector Size (e.g. 4k)
Testing Deduplication / Compression
Emulating other I/O Tool Behaviors

## Slide 11: General Command Format
Write then read/verify data:
  # dt of=PATH bs=value limit=value …
Read/verify previously written data:
  # dt if=PATH bs=value limit=value …
Write without doing read/verify pass:
  # dt of=PATH bs=value disable=verify …
Read without doing data comparison:
  # dt if=PATH bs=value disable=compare …
Execute a predefined workload:
  # dt of=PATH,PATH,… workload=san_disk
Execute a script file:
  # dt script=FILE

## Slide 12: Several Preferred Test Options
Key Test Options:
  bs=random pattern=iot prefix=“%d@%h”
  alarm=6 noprogt=15s noprogtt=180s
  slices=16 history=5 history_data=128
  enable=btags enable=syslog,history_timing
  disable=stats enable=job_stats job_log=FILE
  disable=pstats notime=fsync,close oflags=trunc
  bufmodes=buffered,cachereads,cachewrites,unbuffered
  iodir=vary iotype=vary maxdatap=75 trigger=…
New Prefix Format Control Strings:
  %s = The device serial number (SCSI)
  %U = A unique UUID (36 bytes formatted)

## Slide 13: Data Pattern Layout

## Slide 14: Internal Data Patterns
13 Data Patterns Cycled Through for each Pass:
  0x39c39c39
  0x00ff00ff
  0x0f0f0f0f
  0xc6dec6de
  0x6db6db6d
  0x55555555
  0xaaaaaaaa Complement of previous data pattern.
  0x33333333 Continuous worst case pattern (media defects)
  0x26673333 Frequency burst worst case pattern #1.
  0x66673326 Frequency burst worst case pattern #2.
  0x71c7c71c Dibit worst case data pattern.
  0x00000000
  0xffffffff
Multiple Slices also Cycles Through Patterns
  slice1 0x39c39c39, slice 2 0x00ff00ff, etc

## Slide 15: Data Pattern Files
There are several predefined data pattern files included in the source kit, containing the following data patterns:
  pattern_0 - psuedo-random pattern.
  pattern_1 - psuedo-random pattern alternating with 0's.
  pattern_2 - all 0s.
  pattern_3 - all 1s (FFH).
  pattern_4 - 16 bit shifting 1 in a field of 0s.
  pattern_5 - 16 bit shifting 0 in a field of 1s.
  pattern_6 - alternating 01 pattern (AAH).
  pattern_7 - byte incrementing (OOH - FFH).
  pattern_8 - encrypted data pattern.
  pattern_9 - psuedo-random pattern1 alternating with 0's.
  pattern_all – concatenation of all of the above patterns.
  pattern_dedup - each pattern file written (bs=4k records=5).
These files are specified with the pattern file (pf=file) option.
Stronger data validation available with block tag feature. (enable=btags)

## Slide 16: IOT Data Pattern
The Logical Block Address (LBA) is encoded in the first 4 bytes of each data block (little-endian byte ordering).
The constant value 0x01010101 is added to the LBA as a seed for subsequent words to generate uniqueness throughout data per block.
Seed multiplied by pass count so changes for each pass, for unique data.
Example:
  % dt of=iot.data count=1 pattern=iot dispose=keep disable=stats
  % od --address-radix=d --format=x4 --width=32 iot.data
  0000000 00000000 01010101 02020202 03030303 04040404 05050505 06060606 07070707
  0000032 08080808 09090909 0a0a0a0a 0b0b0b0b 0c0c0c0c 0d0d0d0d 0e0e0e0e 0f0f0f0f
  0000064 10101010 11111111 12121212 13131313 14141414 15151515 16161616 17171717
  0000096 18181818 19191919 1a1a1a1a 1b1b1b1b 1c1c1c1c 1d1d1d1d 1e1e1e1e 1f1f1f1f
  0000128 20202020 21212121 22222222 23232323 24242424 25252525 26262626 27272727
  0000160 28282828 29292929 2a2a2a2a 2b2b2b2b 2c2c2c2c 2d2d2d2d 2e2e2e2e 2f2f2f2f
  0000192 30303030 31313131 32323232 33333333 34343434 35353535 36363636 37373737
  0000224 38383838 39393939 3a3a3a3a 3b3b3b3b 3c3c3c3c 3d3d3d3d 3e3e3e3e 3f3f3f3f
  0000256 40404040 41414141 42424242 43434343 44444444 45454545 46464646 47474747
  0000288 48484848 49494949 4a4a4a4a 4b4b4b4b 4c4c4c4c 4d4d4d4d 4e4e4e4e 4f4f4f4f
  0000320 50505050 51515151 52525252 53535353 54545454 55555555 56565656 57575757
  0000352 58585858 59595959 5a5a5a5a 5b5b5b5b 5c5c5c5c 5d5d5d5d 5e5e5e5e 5f5f5f5f
  0000384 60606060 61616161 62626262 63636363 64646464 65656565 66666666 67676767
  0000416 68686868 69696969 6a6a6a6a 6b6b6b6b 6c6c6c6c 6d6d6d6d 6e6e6e6e 6f6f6f6f
  0000448 70707070 71717171 72727272 73737373 74747474 75757575 76767676 77777777
  0000480 78787878 79797979 7a7a7a7a 7b7b7b7b 7c7c7c7c 7d7d7d7d 7e7e7e7e 7f7f7f7f
  0000512
  %

## Slide 17: Slices Feature (for Files or LUNs)
Each Slice is a Separate Range of Blocks (Capacity or Limit / # of Slices)
Example:
  # dt of=${DT_DEVICE} bs=random slices=2 slice=2 enable=debug disable=scsi,stats
  00m00.00s dt (j:0 t:0): Cloning device 0x1d693010
  00m00.00s dt (j:0 t:0): BLKSSZGET Sector Size: 512 bytes
  00m00.00s dt (j:0 t:0): BLKGETSIZE Capacity: 2097152 blocks (512 byte blocks).
  00m00.00s dt (j:0 t:0): Data limit set to 1073741824 bytes (1024.000 Mbytes), 2097152 blocks.
  00m00.00s dt (j:0 t:0): Cloning device 0x1d69d140 - /dev/mapper/3600a098042425457422443696a6b394f...
  00m00.00s dt (j:0 t:0): The Monitor Thread ID is 0x4175c940
  00m00.01s dt (j:1 t:1): Starting I/O, Job 1, Thread 1, Thread ID 0x4185d940
  00m00.01s dt (j:1 t:1):
  00m00.01s dt (j:1 t:1): Slice 2 Information:
  00m00.01s dt (j:1 t:1): Starting offset: 536870912 (lba 1048576)
  00m00.01s dt (j:1 t:1): Ending offset: 1073741824 (lba 2097152)
  00m00.01s dt (j:1 t:1): Slice length: 536870912 bytes (1048576 blocks)
  00m00.01s dt (j:1 t:1): Data limit: 536870912 bytes (1048576 blocks)
  ...
  00m28.18s dt (j:0 t:0): Terminating with exit code 0...
  00m28.18s dt (j:0 t:0): Exiting with status 0...
  #

## Slide 18: Shared LUN (Multi-Initiator) Testing

## Slide 19: Block Tags (btags) Feature
Block tags provides self-describing data
Block tag is applied to start of each block
Pattern strings and data pattern follow btag

## Slide 20: SCSI LUN Block Tag Format
# ./dt of=/dev/dm-0 bs=random limit=25m enable=btags pattern=iot prefix="%d@%h" disable=scsi_info,stats
# ./dt if=/dev/dm-0 records=1 enable=dump_btags offset=10m disable=scsi_info,stats
dt (j:1 t:1):
dt (j:1 t:1): Block Tag (btag) @ 0x000000000aa88000 (128 bytes):
dt (j:1 t:1):
dt (j:1 t:1): LBA ( 0): 20480 (0x5000)
dt (j:1 t:1): Offset ( 0): 10485760 (0xa00000)
dt (j:1 t:1): Device ID ( 8): 0x0000fd00
dt (j:1 t:1): Serial Number ( 16): BBTWB$Cijk9N
dt (j:1 t:1): Host Name ( 32): ssan-rhel5u4-21
dt (j:1 t:1): Signature ( 56): 0xbadcafee
dt (j:1 t:1): Version ( 60): 1
dt (j:1 t:1): Pattern Type ( 61): 1 (IOT)
dt (j:1 t:1): Flags ( 62): 0x4 (disk,prefix,sequential,forward)
dt (j:1 t:1): Write Start (secs) ( 64): 0x56a680c5 => Mon Jan 25 15:08:37 2016
dt (j:1 t:1): Write Time (secs) ( 68): 0x56a680cb => Mon Jan 25 15:08:43 2016
dt (j:1 t:1): Write Time (usecs) ( 72): 0x000de775
dt (j:1 t:1): IOT Seed ( 76): 0x01010101
dt (j:1 t:1): Generation ( 80): 1 (0x00000001)
dt (j:1 t:1): Process ID ( 84): 25303 (0x000062d7)
dt (j:1 t:1): Job ID ( 88): 1 (0x00000001)
dt (j:1 t:1): Thread Number ( 92): 1 (0x00000001)
dt (j:1 t:1): Device Size ( 96): 512 (0x00000200)
dt (j:1 t:1): Record Index (100): 48640 (0x0000be00)
dt (j:1 t:1): Record Size (104): 104448 (0x00019800)
dt (j:1 t:1): Record Number (108): 81 (0x00000051)
dt (j:1 t:1): Step Offset (112): 0 (0)
dt (j:1 t:1): Opaque Data Type (120): 0 (No Data Type)
dt (j:1 t:1): Opaque Data Size (122): 0 (0x0000)
dt (j:1 t:1): CRC-32 (124): 0xbad347b9
dt (j:1 t:1):
#

## Slide 21: A Block Tag Error Example
01m29.21s dt /dev/sdf (j:2 t:1): Block Tag (btag) @ 0x0000000010368800 (128 bytes):
01m29.21s dt /dev/sdf (j:2 t:1):
01m29.21s dt /dev/sdf (j:2 t:1): LBA ( 0): 990622 (0xf1d9e)
01m29.21s dt /dev/sdf (j:2 t:1): Offset ( 0): 507198464 (0x1e3b3c00)
01m29.21s dt /dev/sdf (j:2 t:1): Device ID ( 8): 0x00000840
01m29.23s dt /dev/sdf (j:2 t:1): Serial Number ( 16): BBTWB+Cijst5
01m29.23s dt /dev/sdf (j:2 t:1): Host Name ( 32): ssan-rhel5u4-21
01m29.23s dt /dev/sdf (j:2 t:1): Signature ( 56): 0xbadcafee
01m29.23s dt /dev/sdf (j:2 t:1): Version ( 60): 1
01m29.23s dt /dev/sdf (j:2 t:1): Pattern Type ( 61): 3 (32-bit pattern)
01m29.23s dt /dev/sdf (j:2 t:1): Flags ( 62): 0x4 (disk,prefix,sequential,forward)
01m29.23s dt /dev/sdf (j:2 t:1): Write Start ( 64): incorrect
01m29.23s dt /dev/sdf (j:2 t:1): Expected: 0x56c4924c => Wed Feb 17 10:31:24 2016
01m29.23s dt /dev/sdf (j:2 t:1): Received: 0x56c49247 => Wed Feb 17 10:31:19 2016
01m29.23s dt /dev/sdf (j:2 t:1): Write Time (secs) ( 68): 0x56c492a5 => Wed Feb 17 10:32:53 2016
01m29.23s dt /dev/sdf (j:2 t:1): Write Time (usecs) ( 72): 0x00052308
01m29.23s dt /dev/sdf (j:2 t:1): IOT Seed ( 76): 0x39c39c39
01m29.23s dt /dev/sdf (j:2 t:1): Generation ( 80): 1 (0x00000001)
01m29.23s dt /dev/sdf (j:2 t:1): Process ID ( 84): incorrect
01m29.23s dt /dev/sdf (j:2 t:1): Expected: 12124 (0x00002f5c)
01m29.23s dt /dev/sdf (j:2 t:1): Received: 12117 (0x00002f55)
01m29.23s dt /dev/sdf (j:2 t:1): Job ID ( 88): 2 (0x00000002)
01m29.23s dt /dev/sdf (j:2 t:1): Thread Number ( 92): 1 (0x00000001)
01m29.23s dt /dev/sdf (j:2 t:1): Device Size ( 96): 512 (0x00000200)
01m29.23s dt /dev/sdf (j:2 t:1): Record Index (100): 196608 (0x00030000)
01m29.23s dt /dev/sdf (j:2 t:1): Record Size (104): 11776 (0x00002e00)
01m29.23s dt /dev/sdf (j:2 t:1): Record Number (108): 7716 (0x00001e24)
01m29.23s dt /dev/sdf (j:2 t:1): Step Offset (112): 0 (0)
01m29.23s dt /dev/sdf (j:2 t:1): Opaque Data Type (120): 0 (No Data Type)
01m29.23s dt /dev/sdf (j:2 t:1): Opaque Data Size (122): 0 (0x0000)
01m29.23s dt /dev/sdf (j:2 t:1): CRC-32 (124): 0xb0eed872
01m29.23s dt /dev/sdf (j:2 t:1): Btag Errors: 2
01m29.23s dt /dev/sdf (j:2 t:1):
Can you see what the root cause of this (false) data corruption is? yep, we’ve all done it, including me! 

## Slide 22: I/O Percentages
Supports read/write and/or sequential/random percentages
Options Added:
  readp=value Percentage of accesses that are reads. Range [0,100].
  'random' keyword makes the read/write percentage random.
  randp=value Percentage of accesses that are random. Range [0,100].
  Sequential accesses = 0%, else random percentage
Please Note: dt I/O enables data verification by default.
  add disable=verify to obtain accurate read/write percentages
Please add flags=direct or bufmodes=unbuffered when testing file systems.
  Note: This is required to avoid reading data from the buffer cache!

## Slide 23: Dynamic Job Control
Used with script files and I/O workload service.
A set of commands to dynamically control jobs
A job is a workload with one to many threads
Jobs can be run asynchronously (background)
  enable=async, “fg”, or “&” for async jobs
Jobs are tracked by a job ID and/or a job tag
  job tags are preferred, since job ID’s vary
  multiple jobs can use the same job tag
    allows controlling sets of jobs via this tag
Log prefix job ID and thread # for tracking
Supports both job logs and/or thread logs

## Slide 24: Job Control Options
Job Start Options:
  istate={paused,running} (Default: running)
    Initial state after thread is created
  tag=string Specify job tag when starting tests.
Job Control Options:
  jobs[:full][={jid|tag}] | [job=value] | [tag=string]
    Show all jobs or a specified job
  cancelall Cancel all jobs
  cancel={jid|tag} | [job=value] | [tag=string]
    Cancel the specified job ID
  modify[={jid|tag}] | [job=value] | [tag=string] [modify_options]
    Modify all jobs or a specified job
    Note: Currently only debug flags and delays can be modified.

## Slide 25: Dynamic Job Control (continued…)
Job Control Options:
  pause[={jid|tag}] | [job=value] | [tag=string]
    Pause all jobs or a specified job
  query[={jid|tag}] | [job=value] | [tag=string] [query_string]
    Query all jobs or a specified job
  resume[={jid|tag}] | [job=value] | [tag=string]
    Resume all jobs or a specified job.
  stopall Stop all jobs
  stop={jid|tag} | [job=value] | [tag=string]
    Stop the specified job
  wait[={jid|tag}] | [job=value] | [tag=string]
    Wait for all jobs or a specified job.

## Slide 26: Workload Definitions
Several workloads ~21 are pre-defined
define command to add new workloads
workload= option to specify a workload
Define your workloads in startup script
workloads command shows defined workloads
Search for workloads via a substring:
  # dt workloads sparse
  Valid Workloads:
  sparse_files: Sparse files test
  bs=16k step=32k disable=pstats enable=lbdata dispose=keep
    …
Execute via:
  % ./dt workload=sparse_files of=/var/tmp/sparse.data limit=1g

## Slide 27: SCSI Specific Features
SCSI Library (from spt) added to dt!
Allows direct SCSI Read/Write CDB’s
  Full SCSI sense data and error recovery
Automatically Gathers:
  Inquiry Information
  Device Identifier
  Serial Number
  Capacity and Block Size
  Helps engineers identify failing disk
TODO: Add NVME API to gather similar info!

## Slide 28: SCSI Options
SCSI Specific Options: (se “dt help” for more options)
  readtype=string The SCSI read type (read8, read10, read16)
  writetype=string The SCSI write type (write8, write10, write16, writev16)
  scsi_recovery_delay=value The SCSI recovery delay. (Def: 2 secs)
  scsi_recovery_retries=value The SCSI recovery retries. (Def: 60)
  scsi_timeout=value The SCSI timeout (in ms).
    Default is 60000 ms, or 60 seconds
Flags to enable/disable:
  scsi SCSI operations. (Default: enabled)
  scsi_info SCSI information. (Default: enabled)
  scsi_io SCSI I/O operations. (Default: disabled)
  sdebug SCSI debug output. (Default: disabled)
  scsi_errors SCSI error logging. (Default: disabled)
  scsi_recovery SCSI recovery control. (Default: enabled)

## Slide 29: SCSI Information Gathered
SCSI Specific Information:
  SCSI Information:
  SCSI Device Name: /dev/sdcs
  Vendor Identification: HGST
  Product Identification: HUH721010AL4200
  Firmware Revision Level: A322
  Target Port Group Support: 0 (ALUA not supported)
  Block Length: 4096
  Maximum Capacity: 2441609216 (9537536.000 Mbytes)
  Provisioning Management: Full Provisioned
  Device Identifier: 5000-cca2-5102-9288
  Device Serial Number: 7PG1DVKR

## Slide 30: Host OS Information Gathered
Reports Host OS Information
Windows:
dt (j:1 t:1): Operating System Information:
dt (j:1 t:1): Host name: MY-MACHINE
dt (j:1 t:1): User name: rtmiller
dt (j:1 t:1): OS information: Windows 7 [6.1.7601 Service Pack 1]
dt (j:1 t:1):
dt (j:1 t:1): File System Information:
dt (j:1 t:1): Volume name: CIFS.HOMEDIR
dt (j:1 t:1): Universal name: \\jade\rtmiller\
dt (j:1 t:1): Filesystem type: FAT
dt (j:1 t:1): Filesystem block size: 4096
dt (j:1 t:1): Volume path name: H:\
_____________________________________________________________________________________________________
Unix:
dt (j:1 t:1): Operating System Information:
dt (j:1 t:1): Host name: ssan-rhel5u4-21
dt (j:1 t:1): User name: rtmiller
dt (j:1 t:1): OS information: Linux 2.6.18-164.el5 #1 SMP Tue Aug 18 15:51:48 EDT 2009 x86_64
dt (j:1 t:1):
dt (j:1 t:1): File System Information:
dt (j:1 t:1): Mounted from device: MY-HOME
dt (j:1 t:1): Mounted on directory: /u/rtmiller
dt (j:1 t:1): Filesystem type: nfs
dt (j:1 t:1): Filesystem options: rw,intr,hard,rsize=8192,wsize=8192,nfsvers=3,timeo=600,tcp,intr,addr=10.60.131.14
dt (j:1 t:1): Filesystem block size: 8192

## Slide 31: Troubleshooting Features
Extended Error Reporting
I/O History with Data and Optional Timing
Corruption Analysis (IOT pattern only)
Corruption Rereads
Loop on Corruptions
Retry All or Select Errors
Triggering Mechanisms
Multiple Debug Flags

## Slide 32: Extended Error Reporting
# ./dt if=/dev/sdaf bs=512k disable=compare enable=scsiio,sense offset=2142569*4k
dt (j:1 t:1):
dt (j:1 t:1): SCSI Information:
dt (j:1 t:1): SCSI Device Name: /dev/sdaf
dt (j:1 t:1): Vendor Identification: HGST
dt (j:1 t:1): Product Identification: HUH728080AL4200
dt (j:1 t:1): Firmware Revision Level: A7D8
dt (j:1 t:1): Target Port Group Support: 0 (ALUA not supported)
dt (j:1 t:1): Block Length: 4096
dt (j:1 t:1): Maximum Capacity: 1953506646 (7630885.336 Mbytes)
dt (j:1 t:1): Provisioning Management: Full Provisioned
dt (j:1 t:1): Device Identifier: 5000-cca2-3b0b-3720
dt (j:1 t:1): Device Serial Number: 2EG656HR
dt (j:1 t:1):
dt (j:1 t:1): ERROR: Error occurred on Wed May 18 17:12:31 2016
dt (j:1 t:1): Read(16) failed on device /dev/sdaf
dt (j:1 t:1): SCSI CDB: 88 00 00 00 00 00 00 20 b2 e9 00 00 00 80 00 00, dir=read, length=524288
dt (j:1 t:1): SCSI Status = 0x2 (SCSI_CHECK_CONDITION)
dt (j:1 t:1): Host Status = 0 (DID_OK), Driver Status = 0x8 (DRIVER_SENSE)
dt (j:1 t:1): Sense Key = 3 = MEDIUM ERROR, Sense Code/Qualifier = (0x11, 0) - Unrecovered read error

## Slide 33: Extended Error Reporting (continued…)
SCSI Specific Error Information with enable=sense (full sense data)
dt (j:1 t:1):
dt (j:1 t:1): Request Sense Data: (sense length 60 bytes)
dt (j:1 t:1):
dt (j:1 t:1): Error Code: 0x72 = Current Error
dt (j:1 t:1): Sense Key: 0x3 = MEDIUM ERROR
dt (j:1 t:1): Additional Sense Code/Qualifie: (0x11, 0) - Unrecovered read error
dt (j:1 t:1): Additional Sense Length: 52 (0x34)
dt (j:1 t:1): Information Field: 2143002 (0x20b31a) <- The actual logical block in error.
dt (j:1 t:1): Command Specific Information: 0 (0)
dt (j:1 t:1): Sense Key Valid: 0x1
dt (j:1 t:1): Sense Key Specific Bits: 0 (0)
dt (j:1 t:1): Sense Key Bytes: 00 7d
dt (j:1 t:1): Error Recovery Type: 0 = Read
dt (j:1 t:1): Secondary Recovery Step: 0
dt (j:1 t:1): Actual Retry Count: 125
dt (j:1 t:1): Field Replaceable Unit Code: 0
dt (j:1 t:1): ili bit: 0
dt (j:1 t:1): Unit Error Code: 0xf72d (63277) <- HGST specific sense descriptors
dt (j:1 t:1): Physical Record Error: 00 01 16 0b 00 1e
dt (j:1 t:1): Cylinder Number: 278
dt (j:1 t:1): Head Number: 11
dt (j:1 t:1): Sector Number: 30
dt (j:1 t:1):

## Slide 34: Extended Error Reporting (continued…)
dt (j:1 t:1): ERROR: Error number 1 occurred on Wed May 18 17:12:31 2016
dt (j:1 t:1): Relative block number where the error occurred is 2142953, offset 8777535488
dt (j:1 t:1):
dt (j:1 t:1): Error Number: 1
dt (j:1 t:1): Time of Error: Wed May 18 17:12:31 2016
dt (j:1 t:1): Read Start Time: Wed May 18 17:12:21 2016
dt (j:1 t:1): Error Code/Message: 0 = Success
dt (j:1 t:1): Pass Number: 1
dt (j:1 t:1): Pass Elapsed Time: 00m10.10s
dt (j:1 t:1): Test Elapsed Time: 00m10.10s
dt (j:1 t:1): File Name: /dev/sdaf
dt (j:1 t:1): Operation: read
dt (j:1 t:1): Record Number: 4
dt (j:1 t:1): Request Size: 524288 (0x80000)
dt (j:1 t:1): Block Length: 128 (0x80)
dt (j:1 t:1): I/O Mode: read
dt (j:1 t:1): I/O Type: sequential
dt (j:1 t:1): File Type: input
dt (j:1 t:1): Device Serial Number: 2EG656HR
dt (j:1 t:1): Device Identifier: 5000-cca2-3b0b-3720
dt (j:1 t:1): Device Size: 4096 (0x1000)
dt (j:1 t:1): File Offset: 8777535488 (0x20b2e9000)
dt (j:1 t:1): Starting LBA: 2142953 (0x20b2e9)
dt (j:1 t:1): Ending LBA: 2143080 (0x20b368)
dt (j:1 t:1): 512 byte LBA: 17143624 (0x1059748

## Slide 35: Corruption Analysis (CA)
Only Supported for IOT Data Pattern
Corruption Analysis Summary
Analyzes IOT Block Data
Side-By-Side Comparison
Dumps 10 Bad Blocks (by default)
Corruption Rereads

## Slide 36: Corruption Analysis Summary
Corruption Analysis (CA) Summary:
  Analyzing IOT Record Data: (Note: Block #'s are relative to start of record!)
  IOT block size: 512
  Total number of blocks: 34 (17408 bytes)
  Current IOT seed value: 0x13131313
  Previous IOT seed value: 0x12121212
  Start of good blocks: 1
  Length of good blocks: 15 (7680 bytes)
  Good blocks file offset: 122765824 (lba 239777)
  Start of corrupted blocks: 16
  Length of corrupted blocks: 19 (9728 bytes)
  Corrupted blocks file offset: 122773504 (lba 239792)
  Number of corrupted blocks: 19
  Number of good blocks found: 15
  Number of zero blocks found: 0 <- Note: Normally indicates unwritten FS blocks!

## Slide 37: Corruption Analysis Options
Corruption Analysis Options:
  boff=string Set the buffer offsets to: dec or hex (Default: hex)
  dfmt=string Set the data format to: byte or word (Default: word)
  dlimit=value Set the dump data buffer limit. (Default: 512 bytes)
  maxbad=value Set maximum bad blocks to display. (default is 10)
  enable=dumpall Dump all blocks (good and bad). (Default: disabled)
Corruption Reread Options:
  retry_delay=value The retry delay. (Default: 5)
  enable/disable flags:
    looponerror Loop on error. (Default: disabled)
    retryDC Retry data corruptions. (Default: enabled)
  for looponerror, the retry delay is multiplied by the retry count
    so with default delay, read/5 sec delay/reread/10 sec delay, etc
    this increasing reread delay reduces the resulting log file sizes

## Slide 38: Retry Error Options
Retry Related Options:
  retry_error=value The error code to retry.
  retry_delay=value The retry delay. (Def: 5)
  retry_limit=value The retry limit. (Def: 60)
  Error Strings Accepted: (example: retry_error=EBUSY)
    Unix OS:
      EIO (5), ENXIO (6), EBUSY (16), ENODEV (19), ESTALE (116)
    Windows OS:
      ERROR_BUSY, ERROR_IO_DEVICE, ERROR_VC_DISCONNECTED, ERROR_UNEXP_NET_ERR, ERROR_SEM_TIMEOUT, ERROR_NETNAME_DELETED
    OR
    retry_error='*' or -1 to retry all errors.

## Slide 39: Trigger Mechanism
Purpose is to Help with Troubleshooting
Designed Initially to Trigger Analyzers
Invoked for I/O Errors, DC, and Long I/O
The trigger control (when to execute).
  trigger_on={all, errors, miscompare, or noprogs} (Default: all)
Triggers Invoked via the Trigger Option:
  trigger=type The trigger to execute during errors.
Example noprog/trigger options:
  noprogt=10s noprogtt=200s alarm=5s trigger=/PATH/dt_noprog_script.ksh

## Slide 40: Trigger Types
Trigger Types Supported:
  br/bdr/lr = Execute a bus/device/lun reset. (SCSI)
  seek = Issue a seek to the failing lba. (SCSI)
  triage = Execute triage operations. (SCSI)
  cmd:string = Execute command or script.
    arguments passed allow intelligent decisions
    most flexible method to roll-your-own actions
    exit status tells dt what to do after script execution
      Note: The exit status is only used for noprog triggers.

## Slide 41: Trigger Script Arguments
Trigger Script invoked with these Arguments:
  dname op dsize offset position lba errno noprogtime
    Where:
    $0 Name of the program.
    $1 dname = The device/file name.
    $2 op = open/close/read/write/miscompare/noprog
    $3 dsize = The device block size.
    $4 offset = The current file offset.
    $5 position = The failing offset within block.
    $6 lba = The logical block address (relative for FS).
    $7 errno = The error number on syscall errors.
    $8 noprogtime = The no progress time (in seconds).
    $9 UserScript - User supplied script to also run (if any).
  exit status: 0 = continue, 1 = terminate, 2 = sleep, 3 = abort

## Slide 42: I/O History Options
Purpose is to record read/write operations.
History Options:
  history=value - Set the number of history request entries.
  history_bufs=value - Set the history data buffers (per request).(or hbufs)
  history_bsize=value - Set the history block data size increment. (or hbsize)
  history_data=value - Set the history data size (bytes to save). (or hdsize)
    the default is to save 32 bytes of record data
Enable/Disable Flags:
  hdump - History dump. (Default: disabled)
    dumps history at end of run when no errors occur
  htiming - History timing. (Default: disabled)
    provides history entry timing information
Plan is to expand this to recording all operations.

## Slide 43: I/O History Example
# dt of=/dev/sdm bs=random count=2 history=5 pattern=iot enable=htiming,hdump disable=scsi,stats
dt (j:1 t:1):
dt (j:1 t:1): Dumping History Data (4 entries):
dt (j:1 t:1):
dt (j:1 t:1): 1403636802.045610 (0.002821) Record #2 - Read 262144 bytes (512 blocks) lba's 512 - 1023 (pos 262144)
dt (j:1 t:1): Offset
dt (j:1 t:1): 000000 00000200 01010301 02020402 03030503
dt (j:1 t:1): 000016 04040604 05050705 06060806 07070907
dt (j:1 t:1):
dt (j:1 t:1): 1403636802.042789 (0.004829) Record #1 - Read 262144 bytes (512 blocks) lba's 0 - 511 (pos 0)
dt (j:1 t:1): Offset
dt (j:1 t:1): 000000 00000000 01010101 02020202 03030303
dt (j:1 t:1): 000016 04040404 05050505 06060606 07070707
dt (j:1 t:1):
dt (j:1 t:1): 1403636802.037960 (0.005431) Record #2 - Wrote 262144 bytes (512 blocks) lba's 512 - 1023 (pos 262144)
dt (j:1 t:1): Offset
dt (j:1 t:1): 000000 00000200 01010301 02020402 03030503
dt (j:1 t:1): 000016 04040604 05050705 06060806 07070907
dt (j:1 t:1):
dt (j:1 t:1): 1403636802.032529 Record #1 - Wrote 262144 bytes (512 blocks) lba's 0 - 511 (pos 0)
dt (j:1 t:1): Offset
dt (j:1 t:1): 000000 00000000 01010101 02020202 03030303
dt (j:1 t:1): 000016 04040404 05050505 06060606 07070707
dt (j:1 t:1):
#

## Slide 44: File System & Buffer Caching
Data buffers are copied to the buffer cache
Therefore writes always complete w/success
  data sync (O_DSYNC) flag can help
Buffer cache data flushed asynchronously
After write pass, flush buffers to detect errors:
  fsync() on Unix systems
  FlushFileBuffers() on Windows
Reads may originate from cache (if still valid)
Direct I/O (DIO) bypasses the buffer cache
Consider DT’s buffer modes option:
  bufmodes={buffered,unbuffered,cachereads,cachewrites}

## Slide 45: Buffer Mode Control
Purpose is to Improve File System Testing
Creative use of Direct I/O (DIO) Feature
Buffer Mode Parameters:
  bufmodes={buffered,unbuffered,cachereads,cachewrites} Sets one or more buffering modes (Default: none)
    buffered = means *no* special flags are added (normal I/O, uses the buffer cache for reads and writes)
    unbuffered = applies Direct I/O (DIO) on both write and read passes (same a flags=direct)
    cachereads = applies DIO flag on write pass only, reads are without DIO (thus cached)
    cachewrites = applies DIO flag on read pass only, writes are without DIO (thus cached)
  Ability to test both buffered and Direct I/O in one invocation

## Slide 47: I/O Monitoring Options
TBA: I/O Monitoring Wiki
The options added to support this feature are:
  noprogt=value - The time in seconds when to report no progress.
  noprogtt= value - The time in seconds when to execute trigger script.
  alarm=value - The time in seconds when to check for no progress.
  trigger=cmd:script - The (optional) trigger script to execute.
  enable=tdebug - Enable timer debug (added to recent versions).
  notime=optype - Disable timing of specified operation type:
    Valid operation types are:
      open close read write ioctl fsync msync aiowait
  Note: Consider adding “notime=close,fsync”
    This avoids timing multiple buffer cache writes

## Slide 48: System Logging
Adding enable=syslog logs start/finish and error msgs to syslog
Useful to correlate dt errors with OS reported errors
Example:
# dt flags=direct pattern=iot bs=random runtime=10 of=/dev/mapper/mpathb enable=btags,raw iotype=vary aios=4 disable=pstats,verbose enable=syslog
…
# tail /var/log/messages
…
Jun 7 15:53:58 cos-lab-test13 dt: 0 20160607 155358 00m00.00s dt (j:0 t:0): Starting: dt flags=direct pattern=iot bs=random runtime=10 of=/dev/mapper/mpathb enable=btags,raw iotype=vary aios=4 disable=pstats,verbose enable=syslog
Jun 7 15:54:08 cos-lab-test13 dt: 50 20160607 155408 00m10.01s dt (j:1 t:1): Finished: dt flags=direct pattern=iot bs=random runtime=10 of=/dev/mapper/mpathb enable=btags,raw iotype=vary aios=4 disable=pstats,verbose enable=syslog
#

## Slide 49: Miscellaneous Updates
  dt file locking options
  dt I/O’s per second (iops=float option)
  stopon=file support for all I/O behaviors (+stopimmed for dt)
  error_file= and master_log= options
  report directory and file i-node’s on errors
  Windows file trim support (to unmap blocks)
  dt now reports max/average no-progress values (avoids external script)
  Higher resolution timer used for start/stop timing, required for short runs with flash
    Note: Previously the clock cycles was used, now the resolution is 10x more accurate! 
  additional format control strings for SCSI and others like workload name

## Slide 50: DT Documentation
Sorry, no active links until I create a web site somewhere!
Documentation available with the DT kit
DT Web Page
DT Overview
DT User’s Guide
DT Use Cases
DT 2013 Update TOI
DT 2014 Update TOI

## Slide 51: Where’s DT Located?
For now, grab from one of our test clients, such as cos-rick.hgst.com
  We keep our tools in /usr/local/bin:
  root@cos-rick:/usr/local/bin# ./dt version
  --> Date: December 21st, 2016, Version: 21.19, Author: Robin T. Miller <--
  root@cos-rick:/usr/local/bin#
DT git Source: (public) Note: This does not include latest WIP changes!
  http://robin.miller@cos-stash-metal/scm/~robin.miller/dt.git